Localization of Sensors
Gaurav Sharma
Rahul Ajmera
Group 5
Department of Computer Science and Engineering
Indian Institute of Technology , Kanpur
8th April 2013

---
Problem Statement
Given a sensor network of N sensors at locations S = {S1, S2,.......,SN}. So, mathematically the localization problem can be formulated as follows: given a multihop network, represented by a graph G = (V, E),and a set of beacon nodes B, their positions {xb, yb} for all b ε B, we want to find the position {xu, yu} for all unknown nodes u ε U.

---
Radio Propagation Model
- ITU Terrain Model.
- Applicable for all terrains.
- Valid for all distances and frequency.
- Handles diffraction due to obstacles.
- Developed on the basis of diffraction theory and first fresnel zone.
- Obstacles in the first fresnel zone will create signals, with a phase shift of 0 to 180 degrees at the receiver.

---
Radio Propagation Model
Formula: A=10-20CN	CN=h/F1	h=hL-hO
F1=17.3 √d1d2/fd	where, f is frequency and A is additional loss due to diffraction.
These losses are summed with Friis transmission equation loss to get overall signal strength.

---
Implemented Algorithms
- APIT
- Diffusion
- Moving Sensor
- Moving Target
- Gradient
- Simulated Annealing
- Centroid

---
APIT
- Node are assumed to be listening to beacons, and storing distances from each one.
- Based on the signal strength, it determines the triangles in which the node lies.
- Centroid of the intersection area of all such triangles is estimated to be the localized coordinates.

---
APIT

---
Diffusion
- Location of a node is centroid of its one hop neighbors.
- Iteratively allocate location of a node to be average of it's neighbors.
- Terminate when steady state is reached, or after a fixed number of loops.

---
Moving Sensor
- A beacon is randomly moved in the grid and it broadcasts its coordinates to the neighbors at all time.
- Every time a node senses the beacon, it generates a new quadratic constraint that it uses to further reduce the uncertainty in its position.

---
Moving Sensor
(a) Node sensing beacon for the first time and constraining itself in the shaded region.
(b) Beacon moves to another location, node senses again and reduces its region.

---
Moving Target
- All the nodes are moved in the grid to detect beacons.
- When it detects a beacon it introduce a bounding box constraint on its position.
- If the node does not encounter any beacon than it bounding box remains the whole grid.
- If a beacon at (x`,y`) after travelling (x,y) than a square bound of side twice the node range is imposed at (x`-x,y`-y).

---
Gradient
- All beacons initiates a gradient by sending its neighbors a message with its location and a count set to one.
- Each recipient remembers the value of the count and forwards the message to its one hop neighbors with the count incremented by one.
- Hence a wave of messages propagates outwards from the beacon, while each sensor maintains the minimum counter value received from all beacons.

---
Gradient
- Hop size of each beacon is calculated by using the number of hops and actual distances from other beacons.
- A error function of two variables x,y for each node is minimized, which is defined by:
  Error = |Σ(x-xi)2+Σ(y-yi)2-Σdi2| summed over all beacon nodes(i).

---
Centroid
- Triangulation of beacons is used, to determine triangle containing the nodes, based on the signal strength.
- Contribution to localization α 1/Area of Triangle
- Fast Algorithm.

---
Simulated Annealing
- System starts from random state and comes to equlibrium.
- A small pertubation (random displacement ) is given to nodes and Cost Function is calculated for that state.
- If cost decreases than new state is accepted but if cost increases than the state is accepted with probability, so that it does not get stuck at local minima.

---
Simulated Annealing
- Cost Function
- Probability Function

---
Results
Accuracy vs Number of Beacons
Percentage Beacons
Percentage Error

---
Results
Accuracy vs Number of Obstacles
Percentage Obstacles
Percentage Error

---
Results
Time vs Number of Beacons
Percentage Beacons
Time per node(seconds)

---
Results
Standard Deviation vs Number of Beacons
Percentage Beacons
Standard Deviation of Error

---
Conclusion
- Based on the qualities required by the system, a cost function of the system can be obtained in terms of accuracy, tolerance due to obstacles, time required for computation and variation in error.
- Based on the obtained cost function an appropriate algorithm could be used which minimizes the cost.

---
Questions?